190h-1e-wifi-hotspot-v2-hl-YY-jm-2024-6-17.odp
Harry Li, Ph.D. ECE
Founder and CEO
CTI One Corporation
Santa Clara, CA 95051
Phone: (650) 463-9892
Version 2, 2024-7-3
CTI One Corporation is located in the Silicon Valley in Santa Clara, California. We design, develop and manufacture AI enabled smart rollators/walkers and exoskeleton devices for mobility solutions.
CTI One Corporation
This document is created by: Harry Li, Ph.D.
Yusuke Yakuwa
Jackson Meng
June. 17, 2024

---
Installing Intel 8265 Wifi Card and FAN on Jetson NANO (3/18,2024)
https://www.google.com/search?q=how+to+install+intell+8265+card+on+jetson+nano&oq=how+to+install+intell+8265+card+on+jetson+nano&gs_lcrp=EgZjaHJvbWUyBggAEEUYOTIJCAEQIRgKGKABMgkIAhAhGAoYoAEyCQgDECEYChigATIJCAQQIRgKGKAB0gEKMjI0MTJqMGoxNagCALACAA&sourceid=chrome&ie=UTF-8#fpstate=ive&vld=cid:ef557009,vid:OOESeo9QH3s,st:0
Intel 8256 Wifi Module beneath the CPU/GPU module
CPU/GPU cooling FAN
25p91 usd Makeronics 8265AC/8265NGW Wireless NIC Module M.2 NGFF for Jetson Nano Support 2.4GHz / 5GHz 300Mbps / 867Mbps Dual Band WiFi and Bluetooth 4.2
https://www.amazon.com/Makeronics-Wireless-Bluetooth-Assembly-Instruction/dp/B07X2NLL85/ref=sr_1_2_sspa?crid=PQPJ05355OP5&dib=eyJ2IjoiMSJ9.FIrh0HTOtcNv-OfjezcaiLPwjT5CtgGr6htwQgeR7cARYkfPJwLszBuI_ETLh6rbhxhF5rjyJf03wOEDLlrmBShPVPOa8Q93zadbI7-2vQ7Z7imengHBG4flyshLVSI9f40yHtVEcPOtmvsiNNtD1jbBEvWfVVmSKZChH2CvB2V9byQbzlgnVWlpJAr_nMT-vVjkr2xZu6Mv4vcgy3yw1enqt6KdgnmsF8eATNO7VjI.c5LE9jQSMua6O--KSehJv5FzqWMdqx4FiERAPw7BALM&dib_tag=se&keywords=intel+8265+wifi+kit&qid=1710823122&sprefix=intel+8265+wifi+kit%2Caps%2C147&sr=8-2-spons&sp_csd=d2lkZ2V0TmFtZT1zcF9hdGY&psc=1

---
Installing Cooling FAN on Jetson NANO (3/18,2024)
2 Pack Dedicated DC 5V Cooling Fan Compatible with NVIDIA Jetson Nano Developer Kit and B01 Version PWM Speed Adjustment Strong Cooling Air Fan
13p50 usd https://www.amazon.com/dp/B07TC21414?psc=1&smid=A2SA28G0M1VPHD&ref_=chk_typ_imgToDp

---
Create Wifi Hot Spot on Jetson NANO (3/18,2024)
Wi-Fi Hotspot Setup - NVIDIA Jetson Developer Kits - YouTube
Amazon affiliate link for Intel 8265 wireless card and antennas: https://amzn.to/3A77tm0
The demo on the youtube is running on a NVIDIA Jetson Nano with an Intel 8265 wireless card. The Jetson is running L4T 32.6.1 an Ubuntu 18.04 variant. The full JetsonHacks Amazon Storefront: https://www.amazon.com/shop/jetsonhac... Website: http://jetsonhacks.com Github: https://github.com/jetsonhacksnano Twitter: Â Â /Â jetsonhacksÂ Â
https://www.youtube.com/watch?v=GAOvGAdwiHk&t=76s

---
Configure Jetson NANO as Wifi AP Router (3/18,2024)
https://chat.openai.com/c/1fe57388-4344-4a0a-a749-6509655e29ac
1. Update your Jetson Nano:
Before starting, it's a good practice to update your system packages to their latest versions:
2. Install hostapd and dnsmasq:
These are the packages needed to set up the access point and DHCP server.
3. Configure hostapd:
Edit the hostapd configuration file:
4. Edit hostapd default configuration:
Edit the hostapd default file to point to the custom configuration file:
5.Configure dnsmasq:
6.Enable IP forwarding:
Edit sysctl.conf:
7. Configure IP tables:
Set up IP forwarding and NAT rules:
8. Save iptables rules:
9. Make iptables rules persistent:
Edit rc.local:
10. then reboot.
General reference for ubuntu machines Wifi AP router https://chat.openai.com/c/3877592f-6c04-458d-8281-0e4b8df8bce6
1. Check your wireless card compatibility:
Make sure your wireless card supports AP mode. Not all wireless cards support this feature.
2. Install necessary packages:hostapd dnsmasq
3. Configure DHCP server:
Edit the dnsmasq configuration file:
4. Configure HostAPD:
Create a configuration file for hostapd:
5. Update hostapd configuration:
Edit the hostapd default file:
6. Enable IP forwarding:
Uncomment the following line in /etc/sysctl.conf:
7. Start services:
8. Configure iptables (if needed):
If you want to share your internet connection, configure iptables:

---
Create Wi-Fi Hot Spot on Jetson NANO Using Commands (6/17,2024)
Step 1: Create the Wi-Fi Hot Spot by running:
$ sudo nmcli device wifi hotspot con-name USB-HS ifname wlan0 ssid jetbot-HS password 11111111
The Marked part could be modified as needed.
Note:
USB-HS is the internal name of the hotspot used by the system.
jetbot-HS is the name of hotspot recognized by the user.
And the password should be at least 8 characters.
When you run the command above, the hotspot should be automatically opened.
Step 2: Open and close the hotspot
The hotspot can be handelly open or closed by running:
$ sudo nmcli connection up USB-HS
$ sudo nmcli connection down USB-HS
Step 3 (Optional): Setting auto-activate the hotspot
The hotspot can be automatically opened when the system boots by editing its configure file:
1. Open the hotspot configure file by running:
$ sudo vim /etc/NetworkManager/system-connections/USB-HS
2.Change the 'autoconnect=false' under 'conenction' section inside the file into ‘true’.
3. Add 'autoconnect = false' to the file of your current connected Wi-Fi file, this will make sure only the hotspot is automatically connected.
4. Restart the network manger by running:
$ sudo systemctl restart NetworkManager

---
Create Wi-Fi Hot Spot on Jetson NANO Using GUI (6/17,2024)
1. Create a Wi-Fi Hot Spot by running:
    1.1. (Start Menu) → Preference → Network Connections
    1.2. Choose a Connection Type: Wi-Fi
    1.3. Input the parameters below in the Wi-Fi tab;
        Connection name: ctione-w100
        SSID: ctione-w100
        Mode: Hotspot
        Band: Automatic (default)
        Channel: default (default)
        Device: wlan0() Choose the USB Wi-Fi module
        Cloned MAC address: (empty) (default)
        MTU automatic (default)
    1.4.Choose the General tab and check if “Automatically connect to this nework when it is available” is on
    1.5. Choose Wi-Fi Security tab, choose WPA & WPA2 Personal, and type Password as “citone2024”
    1.6. Push the Save button
2. Start the hotspot
    2.1 Click the network icon at the bottom right of screen
2.2 Choose ctione-w100
      ctione-w100 Wi-Fi network will start
Step 3 (Optional): Setting auto-activate the hotspot
Turn off auto activate of other Wi-Fi connection
3.1 (Start Menu) → Preference → Network Connections
3.2 Choose one of Wi-Fi connections
3.3 Choose the General tab and check off “Automatically connect to this nework when it is available”
Repeat 3.2 and 3.3 to turn off not hotspot connection’s auto-activate
The hospot Wi-Fi provides: 10.42.0.0/24 network by default and W100’s IP address is 10.42.0.1

---
Reference URL (6/13,2024)
Wi-Fi Hotspot Setup – NVIDIA Jetson Developer Kits
https://jetsonhacks.com/2021/10/05/wi-fi-hotspot-setup-nvidia-jetson-developer-kits/
Creating Wifi AP Hotspot on Jetson Nano
https://forums.developer.nvidia.com/t/creating-wifi-ap-hotspot-on-jetson-nano/72982

---
Discontinued Market Status of Intel 8265 and Its Replacement AX200NGW
(7/8-6/13,2024)
https://www.intel.com/content/www/us/en/products/sku/94150/intel-dual-band-wirelessac-8265/specifications.html
There is, in fact, a replacement module that represents a good upgrade. The Intel AX200 module (~US$20 on Amazon: https://www.amazon.com/Intel-Network-AX200-NGWG-NV-AX2002230-Retail/dp/B07ZVYKRW9) adds support for Wireless-AX and WiFi 6 and improves speed potential to 2.4Gb/s.