Part I
Ammonia (NH3) Sensor Design
Hua Harry Li, Ph.D

---
ammonia/ammonium electrode
Cat No. S-05722-16 model 9512BNWP
1. For both drinking water and wastewater applications
2. EPA-approved for ISE analysis of wastewater
3. The Orion ammonia electrode is extremely durable with a chemical-resistant translucent body.
4. The easy-to-fill electrode comes marked with a fill line to avoid overfilling and to monitor the fill solution level without disassembling the electrode.
5. Membrane replacement options include cost-saving loose membranes or preassembled electrode body with membrane for the convenience of not having to install your own membrane.
20 replacement membranes, preassembled electrode body with membrane, 60-mL of filling solution, and 1-m cable with BNC connector.
Ammonia (NH3)
Ammonium (NH4+)
620
http://www.coleparmer.com/Product/Thermo_Scientific_Orion_ISE_ammonia_ammonium_electrode_with_BNC_connector/EW-05722-16

---
Ammonia/Ammonium Electrode Technical Specs
Product Type	Ion-Selective Electrodes, Gas Sensing
Model and connector	9512BNWP; BNC connector
Concentration	5 x 10–7 to 1 M (10.00 to 17,000 ppm)
Temperature	0-60 degree C
pH range	1 – 12
Interference	Volatile amines
1-800-323-4340

---
Typical NH3 Calibration Curve

---
NH3 Electric Characteristics from Calibration Curve
NH3 Concentration (M)
10 -1
ppm
10 -7
mV
65 mV
350 mV
Note: (1) no external power supply for the electrode.
http://www.coleparmer.com/Product/Oakton_pH_electrode_epoxy_body_sealed_single_junction_general_purpose_3_ft_0_9_m_cable_BNC_connector/S-35801-00#Brochure
Harry Li, Ph.D.

---
OpAmp Circuit Design for NH3
STEP 1: Remove the offset (65 mV)
NH3 Concentration (M)
10 -1
10 -1
ppm
ppm
10 -7
10 -7
285 mv (=350-65)
65 mV
350 mV
10 -1
ppm
STEP 2: Enlarge the dynamic range from [0,285mV] to match ADC's [0,3.3v] range
10 -7
3.3 v

---
OpAmp Design for Step 1
STEP 1: Remove the offset (65 mV)
NH3 Concentration (M)
10 -1
10 -1
ppm
ppm
10 -7
10 -7
285 mv (=350-65)
65 mV
350 mV
Summing OpAmps as level shifter to shift offset 65 mv to 0v.
(1) Using inverting configuration,
A = - (Rf/R1+Rf/R2), where R1 and R2 are resistors for the input 1 and 2; (2) input 1 is for level shifting; e.g.
Vo = V1 (- Rf/R1) … (1)
Where Vo = 65 mV; V1 = 5v;
So
65 x 10 -3 = - (Rf/R1) 5 … (2)
Let
Rf = 1 k Ohm
Hence
R1 = 77 k Ohm (=76.923 k Ohm)
While for input 2, use voltage follower, R2=Rf (=1 k Ohm)

---
OpAmp Design Step 2 for NH3
10 -1
ppm
STEP 2: Enlarge the dynamic range from [0,285mV] to match ADC's [0,3.3v] range
Note: (1) the gain calculation, from 285 mv to 3.3 v, e.g., A = 11.58 choose r4 = 11.58k and r5 = 1k
The design is given on the next slide.
10 -7
285 mv (=350-65)
10 -1
ppm
10 -7
3.3 v

---
Circuit Design for NH3 Sensor

---
Simulation Result
The output: 3.3V
The input offset 65mV

---
Appendix OpAmp Basic Building Blocks
1. to be able to shift the curve; 2. to be able to provide gain to cover ADC full range operation.